# ELECTRIC LOCKING SYSTEM EQUIPMENT

# 1	GENERAL

## 1.1	QUALIFICATIONS

The Electric Locking Systems (ELS) as specified this section is based on products manufactured by:

Dortronics Systems, Inc.

1668 Sag Harbor Turnpike

Sag Harbor, NY  11963

Tel:	(800) 906-0137

(631) 725-0505

Fax:	(631) 725-8148

Web:	www.dortronics.com

The Electric Locking Systems Contractor shall base his bid on the system hardware as specified herein.

Delete sections below if alternate products are not acceptable on this project.

Alternate techniques, modifications, or changes to any aspect of these specifications shall be submitted as a voluntary alternate.

Voluntary alternates shall be fully documented and submitted to the Owner or Owner’s representative, at least ten (10) working days prior to bid

## 1.3	RELATED SECTIONS

- Section 08110 - Steel Doors and Frames.

- Section 08210 - Wood Doors.

- Section 08300 - Special Doors.

- Section 08400 - Entrances and Storefronts.

- Section 08710 - Finish Hardware.

- Section 16000 - Special Security Control Equipment.

## 1.4	REFERENCES

Delete references from the list below that are not actually required by the text of the edited section.

- ANSI/DHI A115 Series - American National Standard Specifications for Steel Door and Frame Preparation for Hardware.

- BHMA A156.2 - American National Standard for Bored and Pre-assembled Locks and Latches.

- BHMA A156.13 - American National Standard for Mortise Locks & Latches; Builders Hardware manufacturers Association.

- BHMA A156.18 - American National Standard for Materials and Finishes.

- Certification Listings:

- Underwriters Laboratories, Inc.

- NFPA 101

- FF-H-106C - Hardware, Builders', Locks and Door Trim, General Specification for.

- The Americans with Disabilities Act of 1992.

## 1.5	SUBMITTALS

Delete any of the following paragraphs not required.

- Submit under provisions of Section 01300.

- Product Data:

- Provide manufacturer's standard details and catalog data demonstrating compliance with referenced standards.

- Provide installation instructions.

- Hardware Schedules: Submit a schedule of products specified in this section coordinated with doors and hardware specified elsewhere.

- Samples:  Submit 1 of each type of electromagnetic lock and accessory device.  The Architect for installation will return approved samples on the final openings of the Project.

- Contract Close-out Submittals:

- As built schedule of locks and accessory devices.

- Operation and maintenance materials.

## DELIVERY, STORAGE, AND HANDLING

Store products indoors in a secured area, and protect from moisture, construction traffic, and damage.

## 1.7	SYSTEM WARRANTIES

All electromagnetic locks shall be guaranteed against defects in material and workmanship with a lifetime warranty after date of manufacture.  All other components of the Electric Locking System shall be similarly warranted for a period of one year.  Expressed warranties are conditionally based on the requirement that the items covered within the guarantee are used and maintained in accordance with the manufacturer’s recommendations.

# PART 2	PRODUCTS

## 2.1	MANUFACTURER

Provide products by Dortronics Systems, Inc.; 1668 Sag Harbor Turnpike, Sag Harbor, NY  11963.  Telephone:  (800) 906-0137 or (631) 725-0505.  Fax:  (631) 725-4234.

## 2.2	ELECTROMAGNETIC LOCKING DEVICES

- #1110 Single door “Maglocks” furnished where scheduled.

- Locks shall be capable of holding a 1200 pound pulling force per door

- The units shall operate on 12 or 24 VDC

- The lock housing shall be constructed to allow connection of all power and control wiring within the removable housing cover.

- The unit shall be no larger than 2” by 1 13/16” by 12 1/2”overall.

- All units shall be supplied with a bi-color LED to indicate lock status

- Furnish a factory installed door position switch concealed within the housing.

- “TJ” locks (top jamb mounted units) shall be supplied with “Z” brackets for in swinging doors where scheduled.

- Supply units with magnetic bond sensors for each door leaf to detect an insufficient holding force on the lock armature.

- Lock housings and mounting hardware (filler plates and angle adapters) shall be standard US28 clear satin anodized aluminum except where special finished hardware is required (see below).

- For additional security the electromagnetic locks shall be supplied with the options described below: (or as scheduled)

Edit, or include schedule showing required locations.

- All above units shall be supplied with a cover tamper switch to detect unauthorized removal of the housing and tamper proof cover screws to deter tamper attempts.

- To alert persons when the door is unlocked for access, a sounder shall be mounted in the lock housing.  This audible alert shall activate on door unlock and cease upon door opening or re-locking of the door. Externally powered.

- For aesthetic design consideration and additional security all above units shall be supplied with “guard housings” to conceal the normally exposed (bottom) edge of the door armature.

- Provide extra length lock housing covers to extend across the full width of opening, or where locks are scheduled to be mounted vertically, from finished floor to door stop or underside of header.

- Provide all above (or as scheduled) electromagnetic locks in finishes as described below:

Edit, or include schedule showing required locations.

- Unless specified otherwise all above lock housings and attachment hardware shall be supplied in standard US28 clear anodized satin aluminum finish.

- All scheduled lock housing attachment hardware and shall be supplied in a dark bronze anodized finish US10B (xDBA).

- All scheduled lock housing attachment hardware and shall be supplied in a satin black anodized finish (xSBA).

- All scheduled lock housing attachment hardware and shall be supplied in a mirror polished chrome finish (xUS26).

- All scheduled lock housing attachment hardware and shall be supplied in a high polished brass finish (xUS3).

- All scheduled lock housing attachment hardware and shall be supplied in a satin chrome finish (xUS26D).

- All scheduled lock housing attachment hardware and shall be supplied in a satin brass finish (xUS4).