# ELECTRIC LOCKING SYSTEM EQUIPMENT

# 1	GENERAL

## 1.1	QUALIFICATIONS

The Electric Locking Systems (ELS) as specified this section is based on products manufactured by:

Dortronics Systems, Inc.

1668 Sag Harbor Turnpike

Sag Harbor, NY  11963

Tel:	(800) 906-0137

(631) 725-0505

Fax:	(631) 725-8148

Web:	www.dortronics.com

The Electric Locking Systems Contractor shall base his bid on the system hardware as specified herein.

Delete sections below if alternate products are not acceptable on this project.

Alternate techniques, modifications, or changes to any aspect of these specifications shall be submitted as a voluntary alternate.

Voluntary alternates shall be fully documented and submitted to the Owner or Owner’s representative, at least ten (10) working days prior to bid

## 1.3	RELATED SECTIONS

- Section 08110 - Steel Doors and Frames.

- Section 08210 - Wood Doors.

- Section 08300 - Special Doors.

- Section 08400 - Entrances and Storefronts.

- Section 08710 - Finish Hardware.

- Section 16000 - Special Security Control Equipment.

## 1.4	REFERENCES

Delete references from the list below that are not actually required by the text of the edited section.

- ANSI/DHI A115 Series - American National Standard Specifications for Steel Door and Frame Preparation for Hardware.

- BHMA A156.2 - American National Standard for Bored and Pre-assembled Locks and Latches.

- BHMA A156.13 - American National Standard for Mortise Locks & Latches; Builders Hardware manufacturers Association.

- BHMA A156.18 - American National Standard for Materials and Finishes.

- Certification Listings:

- Underwriters Laboratories, Inc.

- NFPA 101

- FF-H-106C - Hardware, Builders', Locks and Door Trim, General Specification for.

- The Americans with Disabilities Act of 1992.

## 1.5	SUBMITTALS

Delete any of the following paragraphs not required.

- Submit under provisions of Section 01300.

- Product Data:

- Provide manufacturer's standard details and catalog data demonstrating compliance with referenced standards.

- Provide installation instructions.

- Hardware Schedules: Submit a schedule of products specified in this section coordinated with doors and hardware specified elsewhere.

- Samples:  Submit 1 of each type of electromagnetic lock and accessory device.  The Architect for installation will return approved samples on the final openings of the Project.

- Contract Close-out Submittals:

- As built schedule of locks and accessory devices.

- Operation and maintenance materials.

## 1.6	DELIVERY, STORAGE, AND HANDLING

Store products indoors in a secured area, and protect from moisture, construction traffic, and damage.

## 1.7	SYSTEM WARRANTIES

All electromagnetic locks shall be guaranteed against defects in material and workmanship with a lifetime warranty after date of manufacture.  All other components of the Electric Locking System shall be similarly warranted for a period of one year.  Expressed warranties are conditionally based on the requirement that the items covered within the guarantee are used and maintained in accordance with the manufacturer’s recommendations.

# PART 2	PRODUCTS

## 2.1	MANUFACTURER

Provide products by Dortronics Systems, Inc.; 1668 Sag Harbor Turnpike, Sag Harbor, NY  11963.  Telephone:  (800) 906-0137 or (631) 725-0505.  Fax:  (631) 725-4234.

## 2.3	ACTUATING CONTROL DEVICES

- Provide 5286 Push Plate Switches as required by the scheduled locks and as described below: All Push Plate controls will be constructed with an 1/8” thick aluminum wall plate with 5/16” thick push pad assembly. Applicable contact configurations listed below.

Narrow Jamb Mount Style

Edit, or include schedule showing required locations.

- #N5286-P14 – 1-3/4”x 4-1/2” Narrow Jamb mount unit with SPDT Alternate Action Switch.

- #N5286-P15 – 1-3/4”x 4-1/2” Narrow Jamb mount unit with SPDT Momentary Switch.

- #N5286-P23DA – 1-3/4”x 4-1/2” Narrow Jamb mount unit with Form Z Delayed Action Switch.

- #N5286-P24 – 1-3/4”x 4-1/2” Narrow Jamb mount unit with DPDT Alternate Action Switch.

- #N5286-P25 – 1-3/4”x 4-1/2” Narrow Jamb mount unit with DPDT Momentary Switch.

- #N5286-AT – 1-3/4”x 4-1/2” Narrow Jamb mount unit with DPDT Adjustable time delay (2-60 seconds)

- #N5286-FT – 1-3/4”x 4-1/2” Narrow Jamb mount unit with DPDT Fixed time delay (30 seconds)

Single gang Style

- #W5286-P14 – 2-7/8”x 4-1/2” 1 Gang unit with SPDT Alternate Action Switch.

- #W5286-P15 – 2-7/8”x 4-1/2” 1 Gang unit with SPDT Momentary Switch.

- #W5286-P23DA – 2-7/8”x 4-1/2” 1 Gang unit with Form Z Delayed Action Switch.

- #W5286-P24 – 2-7/8”x 4-1/2” 1 Gang unit with DPDT Alternate Action Switch.

- #W5286-P25 – 2-7/8”x 4-1/2” 1 Gang unit with DPDT Momentary Switch.

- #W5286-AT – 2-7/8”x 4-1/2” 1 Gang unit with DPDT Adjustable time delay (2-60 seconds)

- #W5286-FT – 2-7/8”x 4-1/2” 1 Gang unit with DPDT Fixed time delay (30 seconds)

Double gang Style

- #D5286-P14 – 4-7/8”x 4-1/2” 2 Gang unit with SPDT Alternate Action Switch.

- #D5286-P15 – 4-7/8”x 4-1/2” 2 Gang unit with SPDT Momentary Switch.

- #D5286-P23DA – 4-7/8”x 4-1/2” 2 Gang unit with Form Z Delayed Action Switch.

- #D5286-P24 – 4-7/8”x 4-1/2” 2 Gang unit with DPDT Alternate Action Switch.

- #D5286-P25 – 4-7/8”x 4-1/2” 2 Gang unit with DPDT Momentary Switch.

- #D5286-AT – 4-7/8”x 4-1/2” 2 Gang unit with DPDT Adjustable time delay (2-60 seconds)

- #D5286-FT – 4-7/8”x 4-1/2” 2 Gang unit with DPDT Fixed time delay (30 seconds)

Round 2-1/2” Dia. Button Single gang Style

- #R5286-P14 – 2-7/8”x 4-1/2” 1 Gang unit with SPDT Alternate Action Switch.

- #R5286-P15 – 2-7/8”x 4-1/2” 1 Gang unit with SPDT Momentary Switch.

- #R5286-P23DA – 2-7/8”x 4-1/2” 1 Gang unit with Form Z Delayed Action Switch.

- #R5286-P24 – 2-7/8”x 4-1/2” 1 Gang unit with DPDT Alternate Action Switch.

- #R5286-P25 – 2-7/8”x 4-1/2” 1 Gang unit with DPDT Momentary Switch.

- #R5286-AT – 2-7/8”x 4-1/2” 1 Gang unit with DPDT Adjustable time delay (2-60 seconds)

- #R5286-FT – 2-7/8”x 4-1/2” 1 Gang unit with DPDT Fixed time delay (30 seconds)

CUSTOM FINISHES & ENGRAVING

5286 STOCK ENGRAVING (ADD):

xE1	ADD "PUSH TO EXIT" in black letters

xE1R	ADD "PUSH TO EXIT" in red letters

xE3	ADD "EXIT" in red letters

xE4	ADD "DOOR RELEASE" in black letters

xE5	ADD "EMERGENCY DOOR RELEASE" in red letters

xE6	ADD for other custom engraving

(SUFFIX)

5286 STANDARD HANDICAP LOGOS

xHCP	Add for blue logo on clear aluminum only

xHCP2	Add for blue logo w/ "push to open" on clear aluminum (d-series only)

xHCP3	Add for white logo on blue enamel  plate w / "push to open" (d-series only)

(engraving on red, black, & dark bronze push plates will be white lettering)

(suffix)

5286 SERIES FINISH OPTIONS

xBRE	Add for baked red enamel finish

xDBA	Add for dark bronze anodized

xSBA	Add for satin black anodized

xUS3	Polished brass finish

xUS4	Satin brass finish

xUS26	Polished chrome finish

xUS26D Satin chrome finish

# PART 3	EXECUTION

## 3.1	INSPECTION AND APPROVAL

Upon successful completion of Electric Locking System installation, the Owner’s authorized representative shall inspect and approve the satisfactory operation of the ELS and related accessories.  Upon receipt of a detailed system adjustment list from the Owner’s authorized representative, the ELS Contractor shall complete required correction of each outstanding item on the system adjustment list.  After all items appearing on the installation/inspection report are completed, the Owner's authorized representative will make an appropriate approval.